Test Method Dxxxx

Romaszewski Oil Bench Oxidation Test

(ROBO)

Version  20080807-BETA

Conducted For

TSTSPON1

TSTSPON2

| LABVALID | V = Valid |
| --- | --- |
|  | I = Invalid |

| TSTOIL | NR = Non-Reference Test Oil |
| --- | --- |
|  | RO = Reference Oil Result |

| Test Number |
| --- |
| Instrument ID: INSTRUID | Test Run Number: RUNNUM |

| Date Completed: DTCOMP | Time Completed: EOTTIME |
| --- | --- |
| Oil Code: OILCODE |
| Alternate Oil Codes: | ALTCODE1 | ALTCODE2 | ALTCODE3 |

In my opinion this test OPVALID been conducted in a manner in accordance with the Test Method Dxxxx. The remarks included in this report describe the anomalies associated with this test.

| Submitted By: | SUBLAB |
| --- | --- |
|  | Testing Laboratory |
|  | SUBSIGIM |
|  | Signature |
|  | SUBNAME |
|  | Typed Name |
|  | SUBTITLE |
|  | Title |

Test Report Cover

Test Method Dxxxx

Romaszewski Oil Bench Oxidation Test

(ROBO)

Form 2

Oil Code: OILCODE

Lab Sample Code: LABOCODE

| Testing Laboratory: LAB | TMC Oil Code: IND |
| --- | --- |
| Date Completed: DTCOMP | Time Completed: EOTTIME |

| Instrument ID: INSTRUID |
| --- |
| Test Run Number: RUNNUM |
| Date of Last TMC Calibration: DTLSTCAL | TMC Calibration Expiration Date: DTCALEXP |

| Operational Parameters |
| --- |
| Test Method-Version | METHVER |
| Vacuum Pump Serial Number | VACPMPID |
| Vacuum Control Valve Total Number of Turns from Open to Close (to the nearest quarter turn), revolutions | VCVTOT |
| Vacuum Control Valve Set Point at Time of Last TMC Calibration (number of turns from open, to the nearest quarter turn), revolutions | VCVATCAL |
| Vacuum Control Valve Set Point for This Test (number of turns from open, to the nearest quarter turn), revolutions | VCVSET |
| SAE J300 Engine Oil Viscosity Classification | SAEVISC |
| Distillates – percent of charge, mass % | DISTPOC |

| Test Results |
| --- |
| New Oil D445 Kinematic Viscosity @ 40oC, cSt | KV40NEW |
| Drain Oil D445 Kinematic Viscosity @ 40oC, cSt | KV40EOT |
| Kinematic Viscosity Increase @ 40oC, cSt % | KV40PINC |
| D5293 Cold Crank Simulator Test Temperature, oC | CCSTEMP |
| Drain Oil D5293 Cold Crank Simulator Apparent Viscosity, cP | CCSVEOT |
| D4684 Mini-Rotary Viscometer Test Temperature, oC | MRVTEMP |
| Drain Oil D4684 Mini-Rotary Viscometer Viscosity, cP | MRVVEOT |
| Drain Oil D4684 Yield Stress, Pa | MRVYSEOT |

Summary of Results

Test Method Dxxxx

Romaszewski Oil Bench Oxidation Test

(ROBO)

Form 3

Oil Code: OILCODE

Lab Sample Code: LABOCODE

| Testing Laboratory: LAB | TMC Oil Code: IND |
| --- | --- |
| Date Completed: DTCOMP | Time Completed: EOTTIME |

| Instrument ID: INSTRUID |
| --- |
| Test Run Number: RUNNUM |
| Date of Last TMC Calibration: DTLSTCAL | TMC Calibration Expiration Date: DTCALEXP |

## Out-of-Limit Data and Time, Test Modifications and Comments

| Number of Comment Lines | TOTCOM |  |
| --- | --- | --- |
| OCOMR001 |

Comment Summary