## Slide 1: Formulae
For each severity adjustment entity,
Xi = ith test result in original units in end-of-test order
Ti = ith test result in appropriate units in end-of-test order
(Ti = Xi unless a transformation is used in which Ti = transformed(Xi ))
Yi = ith standardized test result
where target and standard deviation are as currently defined for the reference oil used in the reference test

## Slide 2: Formulae (continued)
For each severity adjustment entity,
Zi = EWMA
For default LTMS, λ = 0.2
Fast start is used, i.e., Z0 = average of Y1 , Y2 , and Y3
ei = prediction error from EWMA

## Slide 3: Chart Constants and Limits
Shewhart Chart of Prediction Error ei = Yi – Zi-1 | 
Limit Type | Limit
Level 3 | 2.066
Level 2 | 1.734
Level 1 | 1.351
EWMA of Standardized Test Result Zi =  (Yi) + (1 - ) Zi-1 |  | 
Limit Type |  | Limit
Level 2 Upper Limit | 0.2 | To Be Determined by Surveillance Panel Input
Level 2 Lower Limit | 0.2 | To Be Determined by Surveillance Panel Input
Level 1 | 0.2 | 0

## Slide 4
LTMS 2nd Edition Flowchart: Target Development
No
Yes
Yes
No
Does study cover sufficient range of technologies, base oils and grades?
Yes
Does study cover sufficient range of labs, stands, engines and test sources of variability?
No
No
Yes
Set reference oil targets based on statistical analysis
Reference oils at or around pass limit?
Yes
No
Yes
Develop precision study and/or Industry Matrix in multiple stages to run
Do the potential reference oils in the study meet chemical and physical constraints of the category?
Does study adequately address questions of interest?
Run matrix stage
Any major problems in which study cannot continue?
Run matrix stage
Statistical analysis of matrix data
Select reference oils
Consider labs and stands for calibration
No
New Test or Oil Development
Calibration
A
Notes: 4

## Slide 5
Run 3 valid reference or matrix tests in the stand uninterrupted by non-reference tests
LTMS 2nd Edition Flowchart: Calibration
Lab based severity adjustment system?
Yes
Yes
Yes
Is the test lab calibrated (existing lab)?
No
Is this a new stand in a lab?
No
No
Yes
No
Yes
No
Set Z0 = Average of first 3 test results in the reference entity
Did the reference test exceed the ei Level 1 limit on any primary test parameter?
This is the first test stand in the lab
This is a stand based severity adjustment system
Is this a new stand?
Run one reference test
Run one reference test
A
Status
E
Status
E
C
B
ei
F
D
Reference Test

## Slide 6
LTMS 2nd Edition Flowchart: Status
Is a
planned reference oil reblend or primary part or fuel being introduced with a reference test?
No
Yes
No
No
Yes
Has it been more than 2 years since the last acceptable reference test in the stand?
Lab based severity adjustment system?
E
Calibration
C
Calibration
B
Calibration
D
Yes
Notes: 6

## Slide 7
Conduct one more reference test in stand that triggered alarm. Do not update charts.
LTMS 2nd Edition: Monitoring (ei) Charts
Did the last reference test exceed the ei Level 3 limit on any primary parameters?
No
Yes
Yes
No
Did the last reference test exceed the ei Level 2 limit on any primary parameters?
Yes
No
Yes
No
Calibration period (number of tests) is 0.80 x standard calibration period
| Yi – Yi+1 | ≤ ei Level 3 limit?
Yi = original value
Update charts
Yi-Yi+1 > ei Level 3 limit and
Yi > Zi-1 ?
Yi = (ei Level 3 limit + Zi-1)
Update charts
Yi-Yi+1 <
- ei Level 3 limit
and
Yi ≤ Zi-1 ?
Yes
No
Yi = (-ei Level 3 limit + Zi-1)
Update charts
A
Undue Influence Analysis
A
F
Zi
G
No

## Slide 8
LTMS 2nd Edition: Adjustment (Zi) Charts
Did the last reference test exceed the Zi Level 2 limit?
No
Yes
No
Yes
No
Did previous valid test (sequencei-1) accomplish calibration and
| ei | ≤ .50 and
| Zi | ≤ .50?
Yes
No
Yes
Calculate SA =
-Zi x industry approved SA standard deviation
Calibration period (number of tests) is 1.4 x standard calibration period
Two or more invalid ref tests in calibration sequence in the same stand?
END
Did previous valid test (sequencei-1) accomplish calibration and | ei | ≤ 0.50 ?
Calibration period (number of tests) is 1.2 x standard calibration period
For all primary parameters
Did the last reference test exceed the Zi Level 1 limit?
No Severity Adjustment
Yes
No
G
Is this a lab based severity adjustment system?
Conduct one more reference test in stand that triggered alarm.
No
Yes
Conduct one more reference test in stand that triggered alarm or in the stand that is next due for calibration.
ei
F

## Slide 9: Flowchart Symbol Legend
        Terminal Point: start, stop, interrupt, delay
        Process: Defined operation
        Decision: Switching operation that determines a number of alternative paths
        Offpage Connector: enter or exit from a page
        Connector: Exit to, or entry from, another part of a page