## Slide 1: Caterpillar Surveillance Panel Meeting
C13, 1Y-4107 Liner Change
Aeration test Update

## Slide 2: ASTM D7549, C13 liner changes
1Y-4107 Liner changes
  Materials change: more consistent graphite
  Casting is changing from static to centrifugal
  New machining line
  New part number
Internal Validation
  Ongoing engine Tests
    Structural, oil consumption, deposits, emissions, etc.
Align the C13 Engine test liner with Production engines
  Ensures part availability and longevity
    Current liners will be available through end of 2016
    New liners can be available starting Q2/Q3 2016

## Slide 3: C13 liners Validation for Standard test, D7549
Proposal: Use new liners in upcoming scheduled reference tests
  Review stand availability and test schedules
  Can we align reference tests to provide multiple data points?

## Slide 4: Aeration Test
Conf Call meeting, Monday, April 11, 2016
MM internal Temperature sensitivity

## Slide 5: Proposed Next Step Experiment
Goal: To confirm LZs observations that the internal MM calibration temperature can effect the density/aeration measurement and to determine calibration method going forward.
Demonstrate the temperature calibration sensitivity with existing stand’s MM (could be run on the last candidate run after 50hrs)
  40-50hrs record the MM internal temperature during a candidate run
  Run experiments after the 50hrs, extend the test length for 10hrs
    (Details on the following page)
  Need to talk with the customers to get their approval. The data will be normalized so it doesn’t reveal any customer information.

## Slide 6: Experiment Details
Run experiments after the 50hrs, extend the test length for 10hrs
    Extend test conditions for 1hr (baseline)
    Adjust the MM internal temperature to 90C for 1hr
    Experiment with large temperature swings (110, 90, 70, 50) 10 minutes at each set point.
    Increase the MM pressure to 150 kpa and sweep temperature (50, 70, 90) internal MM temperature with 10 minutes at each set point.
    Return all the MM internal temperature calibration settings back to the original with the pressure back at 84 kpa and run for one hour collecting data.
Potential next step: Run warm-up MM temperature calibration LZ experiment (run with LZ oil and calibration procedure)
  Run prior to referencing