UNAPPROVED MEETING MINUTES OF THE

Cummins Surveillance Panel

San Antonio, Texas

January 24, 2007

THIS DOCUMENT IS IN THE PROCESS OF DEVELOPMENT AND IS FOR ASTM COMMITTEE USE ONLY.  IT SHALL NOT BE REPRODUCED, CIRCULATED OR QUOTED, IN WHOLE OR IN PART, OUTSIDE OF THE ASTM COMMITTEE ACTIVITIES, EXCEPT WITH THE APPROVAL OF THE COMMITTEE HAVING JURISDICTION OR THE PRESIDENT OF THE SOCIETY.

# Action Items

- Update Scope and Objectives

- Address change in oil filter adapter

- Update test procedure with latest changes and submit for approval

- Modify soot correction equation for ISB (see below)

- Cummins to determine why block stiffener plate was removed from latest batch of engines

- TEI to assign a part number for the ISM engine that correlates to the correct CPL number

- Operationally valid/non-interpretable tests will count towards stand use between calibration tests

- Submit to sub-committee B for approval an information letter changing the stand calibration period from 18 months to 12 months

# Call to Order/Membership/Approval of Minutes

Jim Moritz called the meeting to order at ~ 11:00 am (CDT). A tentative agenda had been distributed via email prior to the meeting.

# Summary of Discussions

The following summarizes the various topics discussed during the meeting:

- The Scope and Objectives will be updated to include monitoring of the ISB and ISM tests and to drop the M-11 HST and M-11 EGR. Objectives will be added as they are needed.

- There was considerable discussion about what to do about the oil filter head change. The old filter head ( part number 3899699) is no longer available in service. The new filter head (part number 3102774) has a different thread dimension and the ISM test filter will not fit. Several suggestions were offered as to how to remedy the situation. Cummins continues to try and find a source for the old style head or possibly a replacement remote mount with no success. The most likely correction will be to fabricate an adapter. Dan Domonkos volunteered to try to come up with a suitable adapter.

- The test procedure needs to be updated to include a precautionary statement about not using the coated rocker box for testing. At one time the rocker box came with a “green” coating which flaked off during testing. The coating needs to be removed prior to using for testing.

- Bob Campbell presented some information regarding pressure calibration tolerances. After some discussion it was agreed to use the recommendations included in the Data Acquisition and Control Task Force Report (DACA II) that is posted on the TMC website.

- The ISM turbo part number has changed to 4955303NX. All of the changes were external and should not affect performance.

- As a follow up to some previous discussions held during recent teleconferences, Jim Rutherford presented some information he had on the ISB soot correction for tappets and crossheads.  Concern has been raised about the current soot correction equations and the impact they are having on final test results and whether that correction is realistic in light of recent calibration tests. In addition to this presentation Jim Moritz presented an analysis he had performed. After some discussion Jim Moritz moved that the following changes be made to the soot correction equation for the ISB:

Change coefficient to 39

Change average of average soot to 3.48

Limit adjustment to 2.92 to 4.04 average soot

Range of Adjustment +/- 21.84 mg

Recalculate reference oil test results

Update targets for PC-10B/831 at 10 tests

Re-run LTMS, no stands become rejected, one becomes acceptable

Effective for all tests started on or after 1/25/07

This motion passed with 10 affirmatives; 0 negatives; 2 waives.

- Ron Buck presented the hardware update for the ISM and ISB. Batch B ISM crossheads have been exhausted and batch C has been received. All current orders were filled using batch B and all new orders will use batch C. The new ISM engines at TEI do not have a block stiffener plate as previous engines did. Dan Nyman agreed to find out what changed in the engine to allow removal of this plate. TEI was requested to assign a unique number to the ISM engines for ordering purpose.

- Jeff Clark presented the TMC report. In addition to the ISB, there are some mild trends on ISM crosshead weight loss and injector adjusting screw weight loss that need to be addressed.  There will be conference calls to address this issue and the group will try to resolve by June.

- The issue of whether or not to count operationally valid/non-interpretable tests towards stand use was discussed. After some debate, the panel agreed that they should count towards stand use. Vote was 8/0/1 ( for/against/waive).

- The panel voted on reducing the calibration period from 18 months to 12 months. The vote was 7/2/2 ( for/against/waive). Since this is an information letter issue and will need to be balloted by Subcommittee B, and because there were negative votes that could potentially result in negative Subcommittee B ballots, this will not become effective until it has been balloted and approved by Subcommittee B.

- The group reviewed draft 9 of the ISM test procedure  and made corrections and changes as needed. The final approved draft will be submitted to the appropriate committee for approval as part of the research report.

# Additional Business/Next Meeting

The next meeting will be at the call of the chairman.