## Slide 1: Ford 6.7L Valvetrain Wear Test Precision Matrix Update
Statistics Group, September 2020

## Slide 2: Statistics Group
Martin Chadwick, IAR
Elisa Santos, Infineum
Jo Martinez, Chevron Oronite
Sean Moyer, TMC
Abaigh Ritzenthaler, Afton
Todd Dvorak, Afton
Travis Kostan, SwRI

## Slide 3: Objective
To adjust the precision matrix to include PC-10 and three different ASTM D975 fuels.

## Slide 4: Executive Summary
The new precision matrix design is shown on slide #6.
This precision matrix design is only capable of detecting large differences due to fuel. If differences in means exist which are less than two standard deviation, these are more likely than not to go undetected by the precision matrix.
The precision matrix is more likely than not to detect variability differences if the standard deviation of D975 results is greater than or equal to 1.56 times the standard deviation of PC-10 results.
Based on #1 and #2, the group needs to consider the potential sizes of the differences in means and standard deviations which could go undetected and determine appropriate actions for monitoring and possibly correcting for these potential differences, or determine if a different path forward for fuel approval is necessary.

## Slide 5: Precision Matrix Change
Fuel A = PC-10 Fuel
Fuel B = ASTM D975 Pump Fuel
Stand A-1 | Stand A-2 | Stand G-1 | Stand G-2
LWO, Fuel B | HWO, Fuel A | HWO, Fuel B | LWO, Fuel A
HWO, Fuel A | HWO, Fuel B | LWO, Fuel A | LWO, Fuel B
HWO, Fuel B | LWO, Fuel A | LWO, Fuel B | HWO, Fuel A
LWO, Fuel A | LWO, Fuel B | HWO, Fuel A | HWO, Fuel B
LWO, Fuel B | HWO, Fuel A | LWO, Fuel A | HWO, Fuel B
Stand A-1 | Stand A-2 | Stand G-1 | Stand G-2
LWO, Fuel B | HWO, Fuel A | HWO, Fuel B | LWO, Fuel A
HWO, Fuel A | HWO, Fuel B | LWO, Fuel A | LWO, Fuel B
HWO, Fuel B | LWO, Fuel A | LWO, Fuel B | HWO, Fuel A
LWO, Fuel A | LWO, Fuel B | HWO, Fuel A | HWO, Fuel B
LWO, Fuel B | HWO, Fuel A | HWO, Fuel B | LWO, Fuel A
Previous Matrix
New Matrix

## Slide 6: Precision Matrix with Three D975 Sources
Fuel B1 = TxLED Diesel
Fuel B2 = Michigan Fuel
Fuel B3 = Virginia Fuel
Stand A-1 | Stand A-2 | Stand G-1 | Stand G-2
LWO, Fuel B2 | HWO, PC-10 | HWO, Fuel B3 | LWO, PC-10
HWO, PC-10 | HWO, Fuel B1 | LWO, PC-10 | LWO, Fuel B1
HWO, Fuel B2 | LWO, PC-10 | LWO, Fuel B3 | HWO, PC-10
LWO, PC-10 | LWO, Fuel B1 | HWO, PC-10 | HWO, Fuel B1
LWO, Fuel B2 | HWO, PC-10 | HWO, Fuel B3 | LWO, PC-10
The table below shows the precision matrix with three D975 fuel sources.
Note:
The task was to design a matrix using three D975 fuels. Use of these fuels here doesn’t mean the stats group agrees/disagrees with these specific choices, as that is a separate discussion from what was asked of the stats group here.

## Slide 7: Power Calculations
Statistical power is the probability of being able to detect a difference at given significance level if the real difference is “X”.
Components of the power calculations done here:
Power (A Probability)
Significance Level (0.05 and 0.10 used here for 95% and 90% confidence, respectively)
The real difference between fuels, unknown in advance, so hypothetical values are used. This difference will be in terms of standard deviations, since the standard deviation is unknown at this time.

## Slide 8: Power Calculations
One D975 fuel different from average of all others.
PC-10 Different from average of all D975.
Difference | 1 Sigma | 1.5 Sigma | 2 Sigma | 2.5 Sigma | 3 Sigma
Power | 15% | 29% | 46% | 64% | 79%
Difference | 1 Sigma | 1.5 Sigma | 2 Sigma | 2.5 Sigma | 3 Sigma
Power | 25% | 42% | 60% | 77% | 89%
Difference | 1 Sigma | 1.5 Sigma | 2 Sigma | 2.5 Sigma | 3 Sigma
Power | 21% | 43% | 66% | 84% | 94%
Difference | 1 Sigma | 1.5 Sigma | 2 Sigma | 2.5 Sigma | 3 Sigma
Power | 34% | 57% | 78% | 92% | 98%

## Slide 9: Variance Testing
If there are no statistically detectable differences in the means of the various fuels, we would next test for variability differences. The table below indicates the minimum ratio of the standard deviations which would be required to statistically detect a difference.
F-Test | Alpha = 0.05 | Alpha = 0.10
One-Sided | 1.78 | 1.56
Two-Sided | 2.01 | 1.78
Assuming we would consider a p-value < 0.10 a concern, we would flag D975 fuels as statistically more variable if the standard deviation* is 1.56 times greater or more than PC-10 fuel results.
* - standard deviation of residuals

## Slide 10: Executive Summary
The new precision matrix design is shown on slide #6.
This precision matrix design is only capable of detecting large differences due to fuel. If differences in means exist which are less than two standard deviation, these are more likely than not to go undetected by the precision matrix.
The precision matrix is more likely than not to detect variability differences if the standard deviation of D975 results is greater than or equal to 1.56 times the standard deviation of PC-10 results.
Based on #1 and #2, the group needs to consider the potential sizes of the differences in means and standard deviations which could go undetected and determine appropriate actions for monitoring and possibly correcting for these potential differences, or determine if a different path forward for fuel approval is necessary.