Modified D6278 30/90 cycle Shear Test Process flow:

# Text boxes

Calculate Vres, Vrun and the counter settings for 30 cycles of 170 ml.(n*30) Calibrate  the gage pressure with RL-34 at 30 total cycles. Adjust flow for Test Oil as necessary. (based on D6278)

Calculate counter settings for 30 cycles of 200 ml (n1*30) and 60 cycles of 170 ml (n*60)

Flush System with 50-75 ml of Candidate fluid twice with reservoir bypassed and oil draining to waste.

Charge reservoir to

Vrun + 30 ml run for 3 mins bleeding out the air.

At 3 mins purge head by bypassing the reservoir to waste.

Calculate n1, number of strokes to pump additional volume one cycle by:

(200/170( *n = n1

Drain for 3 mins and remove thermometer.

Adjust the oil level to Vrun and run for 0.5*n to verify flow rate. Drain to waste.

Adjust the volume to (Vrun + 30 ml) in Reservoir and then replace the Thermometer.

Set counter to

(n1 * 30) cycles.

Return bypass valve to flow into the reservoir and start the pump.

When 30 cycle test is comp. Drain 10-15 ml to waste then drain to a sample bottle (A) down to Vrun.

Reset counter to (n * 60) and restart the test to complete the 90 –cycle total.

When the remaining 60-cycles are comp. Drain 10-15 ml to waste and drain to a sample bottle (B) the remaining oil in the reservoir.

Run D445 KV at 100°C on Fresh Oil, Sample A and Sample B all in the same tube.

Charge with Vrun + 60 ml, pump 50 ml to waste