Mack T-13 Test Instructions Outline, Rev.8

- Engine Configuration

  - Engine mounted with flywheel perpendicular to floor and tilted 4° side-to-side toward intake manifold

  - PVD Coated Exhaust Rocker Arms, P/N 21809012 with PVD Coated Rocker-Arm Shaft, P/N 21534995

  - Remove thermostat and replace it with sleeve P/N 21474103 (see attached) and seal P/N 1549651

  - US07 Oil Filter Housing P/N 21183257 with mods including removal of oil temperature thermostat

  - No-Brake Camshaft P/N 21219818 with “Dummy” Solenoid Valve P/N 21105100

  - Remove housing element with heater attached to intake manifold and replace it with:

    - Intermediate Housing w/o Pre-Heater, P/N 20730387

    - Bolts, P/N 965184

    - Washers, P/N 976944

    - Gaskets, P/N 3979639

  - Oil Mist Separator speed detection (2 pulses per revolution):

    - Speed Sensor Bracket – Detroit Diesel P/N A4720180340

    - Speed Sensor - Detroit Diesel P/N A0061535528

    - Speed Sensor Connector - Detroit Diesel P/N A0001506336

  - Front Mount Steel Oil Pan P/N 21585801 with Gasket P/N 21293367, pick up height, oil sump thermocouple and oil drain set per attached dimensions (target 3,000-3,500 grams after 1 hour at test conditions)

    - Oil level sensor to be removed

  - Coolant, Chevron Delo Extended Life Coolant diluted 50/50

    - P/N 227811 (50/50 pre-mixed)

    - P/N 227808 (concentrated)

  - Coolant Filter w/o additives, Volvo P/N 21388479 21937327

  - Full Flow Oil Filter (2), P/N 21707136

  - By-Pass Oil filter, P/N 21707135

  - Compressor Block-Off Plate, Volvo Penta P/N 21226107

  - Turbocharger Inlet Rubber Hose P/N 21659720

  - Damper Cooling Fan

  - Cylinder Head, P/N 21458124, EU6 21995786

  - Cylinder Head Kit, P/N 21460896, (EU6) P/N 22251160 22498402

  - Valve Stem Seal P/N 21990221

  - Injector (6), P/N 21458369 22027808, reman # 85013612. Use Graphite paste P/N 85134750 for installation.

  - Turbocharger, P/N 85128135 85136177 85141061 with Gasket with large opening P/N 20781146

  - Oil Cooler, ITT Model SSCF 5-160-03-014-004 Two pass, All Stainless steel

    - Remove cooler core and baffle from engine (right side)

    - Max length of combined 1” (No. 16 Aeroquip or equivalent)  flex lines to/from cooler to be 36”

  - Oil Gallery Thermocouple insertion depth: middle of oil gallery at 2.5265 “ from face of engine block

  - Fuel Gallery Thermocouple insertion depth: 2.00“ from face of cylinder head

  - Oil Jet Thermocouple insertion depth: 3.0925“ from face of oil filter housing

  - Oil Cooler Out Thermocouple insertion depth: 0.950“ from face of oil filter housing

  - Coolant Out Thermocouple to be located midstream in the 4 bolt flange of the coolant outlet pipe

  - Remove vanes and cartridge from fuel&steering pump assembly

  - External Oil System Pumps, same as Mack T-12 with exception of line from oil pan to weigh tank (suction line) be No. 12 size (Inside Diameter 16 mm)

    - Return line from external oil vessel connected to center of compressor block-off plate

    - Vent of external oil vessel connected to cylinder head cover between cylinder 1 and cylinder 2 (see attached)

    - Max length of supply and return line combined: 18’ (5.4 m)

  - Flywheel, P/N 20941525 21514067

  - Use Mack Valve Cover P/N 20728586

  - Crankcase pressure port located on cylinder head cover between cylinder 3 and cylinder 4

  - Crank pulley P/N 20799474, fan pulley P/N 20872502, belt idler (including pulley) P/N 20582550, belt tensioner P/N 21779276, belt P/N 88GB447P615 for correct water pump speed

  - Compressor Discharge Temp Sensor (see attached table)

  - Boost Pressure Sensor, (see attached table)

  - Leave Ambient Temp Sensor disconnected

  - Engine coolant through turbocharger (standard factory set-up)

  - Aftertreatment fuel doser removed.  Connector jumper? Yes.  Run with fault codes (running fault codes in attached table)

  - Intertek Design EGR cooler adapter

  - Fuel Filter Housing P/N 21336013

  - Fuel Filter P/N 20972295

  - Fuel Water Separator P/N 21380521 (plastic bowl/drain P/N 21337071)

  - Oil Sampling Port

    - Size: ¼” (No. 4 Aeroquip or equivalent)

    - Max. Length: 8’

    - Port Location (see attached): pre-filter pressure port

  - Pressurized Oil Filling Connection (see attached): between oil cooler and oil filter housing on return to filter housing

  - Charge Air Cooler

    - Specifications:

      - Pressure drop at test conditions ≤ 5 kPa;

      - Provide enough cooling capacity to maintain specified Intake Manifold temperature;

      - Equipped with drain to remove condensate.

  - CO2 Intake and Exhaust Measurements

    - Same probe specifications as Mack T-12;

    - Cool sample to a Dew Point ≤ 5°C

- List of PCU and Bearing P/N’s provided by Ken (needs to be verified against the list provided by Allison):

  - Piston – 21170742 P06 (6)

  - Liner – 20852790 P05 (6)

  - Rings – top – 21251596 P03 (6)

    - second – 20590309 P32 (6)

    - oil - 20568155 P34(6)

  - Pin – 20569833 P32 (6)

  - Snap Rings – 914531 P01 (12)

  - Liner Seals – top at flange – 470922 P03 (6)

    - lower – top and middle – 470190 P05 (12)

    - lower – bottom – 21430623 P01 (6)

  - Main Bearings – Upper – 20530902 (7)

    - Lower – 20530900 (7)

  - Rod Bearings – Upper – 20508264 (6)

    - Lower – 20530094 (6)

- Test Stand Configuration and Test Operation

  - 1500 rpm, 2200 Nm, 3000 psi, “3573E09A59_t13_Rev9_1500_3000psi_ “ Flash file

  - Mack T13 Test Development AL824MOD01 V11a.xls test protocol

  - Cam-Crankshaft Timing Verification

  - Controlled Parameters:

    - CO2 Intake Manifold: 2.06 ± 0.05 %

    - Intake Manifold Pressure: 232 ± 5 kPaG

  - Ranged Parameters:

    - Exhaust Pipe: TBD (range from 5 tests with 821-3: 10.57-11.23%)

  - Active EGR and VGT Control

    - Use VGT and EGR valve to control Intake Manifold CO2 and Intake Manifold Pressure

  - Test Length: 360-h

  - Both external oil vessel and external oil cooler to be drained at completion of Break-In

#1 – EGR Delta Pressure Sensor - Must use sensor PN# 21713917 with new harness.

NOTES

- FYI - #4 and #5 Position sensors - are reversed for position on MP8 Engine /Sensor display above.

- #6 sensor: the correct PN# is 21521353.  Remove sensor from oil pan.

- #13 – is not used

- #14 – is not used

Ambient Air Temperature Sensor to be left disconnected

External Oil System Suction Port

Oil Sump Thermocouple Location

Oil Sampling Port

Pressurized Oil Fill Location

Sleeve replacing Thermostat

# Text boxes

Sampling Port

Filling Port