## Slide 1: LSPI Precision Matrix + Non-PM Data Analysis
Statistics Group
Mar 24, 2017

## Slide 2: Statistics Group
Arthur Andrews, ExxonMobil
Doyle Boese, Infineum
Jo Martinez, Chevron Oronite
Kevin O’Malley, Lubrizol
Martin Chadwick, Intertek
Richard Grundza, TMC
Lisa Dingwell, Afton
Todd Dvorak, Afton
Travis Kostan, SwRI

## Slide 3: Thoughts from Stats Group
The test discriminate oils and shows adequate repeatability.
Issues that the Stats Group could not reach a consensus:
With or without engine hour adjustment
Oil to use in the model to estimate precision and LTMS targets (with or without 220)
  220 is not a reference oil used for Severity Adjustment
  Fail to estimate precision in the range of results if we don’t include 220

## Slide 4: With Engine Hour Effect

## Slide 5: Summary
Data utilized is 221 and 222 Precision Matrix and non-Matrix data (n = 24).
LSPI transformed as Ln[AVPIE + 1] and Sqrt[AVPIE + 0.5] was regressed on Lab, Stand[Lab], Engine[Stand, Lab], Oil, and EngHrs.
  p-Values for EngHrs were 0.13 and 0.15.
Engine hour term is borderline statistically significant
  Regardless of practical data subset, EngHr coefficient is negative.
  Plots on following slides indicate consistent negative correlation between AVPIE and EngHrs.

## Slide 6: Average LSPI Versus Engine Hours
The slopes for both 221 and 222 have slight negative slopes.

## Slide 7: Average LPSI Versus Engine Hours by Engine
Of the 4 engines with substantial engine hours, 3 showed a negative slope.

## Slide 8: Average LSPI – LS Mean Versus Engine Hours
Only 221 and 222 results are plotted.
Each of the 4 engines with substantial run time have negative slopes.

## Slide 9: Average Fuel Flow Versus Engine Hours
Average Fuel Flow was used a factor as a replacement for Engine Hours in a regression model but did not explain nearly as much variation.
Fuel Flow was added as a factor to the model with Engine Hours (and the other terms) with both being statistically significant but had VIFs between 3 and 4.

## Slide 10: Regression Details
Ln[AVPIE + 1]
n = 24
RMSE = 0.1387
Engine Hour Coefficient = -0.0002287
Sqrt[AVPIE + 0.5]
n = 24
RMSE = 0.2869
Engine Hour Coefficient = -0.000445

## Slide 11: Without Engine Hour Effect

## Slide 12: ENHRS and FUEL FLOW Correlation

## Slide 13: No indication of FUEL FLOW effect
Note: Residuals from Oil, Lab model (n=34)

## Slide 14: Model: Oil Lab Engine(Lab)
220, 221, 222
221, 222

## Slide 15: Model: Oil Lab
220, 221, 222
221, 222

## Slide 16: ENHRS Effect
ENHRS effect is influenced by a single Non-PM test with the highest engine hours (1071). Without this data, ENHRS is not statistically significant.
There’s a gap in the data between 700-1000 hours.
More appropriate data is needed to ensure correct estimation of ENHRS effect.

## Slide 17: LSPI Precision Matrix Statistical Analysis

## Slide 18: Executive Summary
Precision Matrix (PM) Analysis Highlights:
  This analysis includes the results of 20 valid precision matrix tests plus an additional 14 non-matrix tests run on identical hardware to the same procedure which were deemed operationally valid by the LSPI development team.
  Data supports the use of Ln(AvPIE+1) transformation or Sqrt(AvPIE+0.5)
  Significant oil differences: 222 > 221 > 220
  Marginal Lab differences; Engine within Lab differences are not statistically significant
  Estimated within an engine test precision
    Ln(AvPIE+1) = 0.2085
    Sqrt(AvPIE+0.5) = 0.2813
  Estimated test precision across labs and engines
    Ln(AvPIE+1) = 0.2101
    Sqrt(AvPIE+0.5) = 0.2856

## Slide 19: LSPI Precision Matrix Original Data Set
  Original Precision Matrix Data Summary:
    3 Labs {A, B, and G}
    3 Reference Oils {220, 221, and 222}
    5 Engines (named here by “LAB-SBLOCKID”)
      {A-LSPI14, A-LSPI15, B-1003, G-PI14, and G-PI15}
    From the original 20-test matrix:
      4 were discovered to have run on different hardware, 6 were deemed operationally invalid. All 10 tests were rerun to arrive at 20 total matrix tests all deemed operationally valid by the LSPI development group.
Notes: Updated

## Slide 20: LSPI Precision Matrix Original Data Set
  Precision Matrix Data Table from Frank Farber’s 20160919 LSPI Matrix Test Status update.
Notes: Updated

## Slide 21: LSPI Precision Matrix – Additional Tests
  On March 9, 2017, the LSPI development group deemed 14 additional tests as operationally valid and viable for inclusion in precision matrix analysis.
    2 Labs {A and G}
    3 Reference Oils {220 (n=3), 221 (n=1), and 222 (n=10)}
    6 Engines (named here by “LAB-SBLOCKID”)
      {A-LSPI13, A-LSPI14*, A-LSPI15*, A-LSPI18, A-LSPI19, and G-PI14*}
        * - precision matrix engine
Notes: Updated

## Slide 22: LSPI Precision Matrix - Additional Tests
  Below is a plot of the matrix and non-matrix data
Notes: Updated

## Slide 23: Raw AvPIE by Engine
Oil ranking is consistent across engines.
Notes: Updated

## Slide 24: Raw AvPIE by Oil
The oils show good separation, with only a small overlap between 221 and 222.
Notes: Updated

## Slide 25
Evaluating the Transformation of AvPIE

## Slide 26: Transformation of AvPIE
Since precision statements and other conclusions made from the ANOVA model are based on the assumption that the model residuals have a Normal distribution with mean zero and constant variance which is independent of response level, often times a transformation is needed to ensure that these assumptions are reasonable.
Example:
Estimated standard deviation of results within an engine.
95% coverage based on a Normal distribution of residuals
Multiplier due to inference on 2 results
Notes: Updated

## Slide 27: Summary of Transformation Evaluation
In the Box-Cox Analysis, the square root transformation is preferred when using all oils and all data. Using only 221 and 222 would make the natural log transformation slightly more favorable.
The square root transformation does a better job of stabilizing the variance across all 3 oils tested, which will be critical to ensure that our test precision statement is representative of all oils to be tested in the future.
The repeatability limits seem much more appropriate with the square root transformation. For the natural log transformation, the windows appear to be too small for low event oils, and too large for high event oils.
Notes: Updated

## Slide 28: Transformation of AvPIE
Model is AvPIE +1 ~ Oil, Lab
The Box-Cox analysis curve suggests that a natural log ( or a square root transformation ( are both reasonable choices.
Analysis is performed with the both the natural log transformation and with the square root transformation for comparison.
Matrix Tests (n=20)
Matrix and Non-matrix (n=34)
Matrix and Non-matrix, 221,222 only (n=24)
Notes: Updated

## Slide 29: Transformation of AvPIE
Model is AvPIE +1 ~ Oil
The Box-Cox analysis curve suggests that a natural log ( or a square root transformation ( are both reasonable choices.
Analysis is performed with the both the natural log transformation and with the square root transformation for comparison.
Matrix Tests (n=20)
Matrix and Non-matrix (n=34)
Matrix and Non-matrix, 221,222 only (n=24)
Notes: Updated

## Slide 30: Ln(AvPIE +1) ~ Oil, Lab Residual Plot by Oil
There variance does not appear similar across all oils.
Notes: Updated

## Slide 31: Ln(AvPIE +1) ~ Oil Residual Plot by Oil
There variance does not appear similar across all oils.
Notes: Updated

## Slide 32: Sqrt(AvPIE+0.5) ~ Oil, Lab Residual Plot by Oil
There variance appears reasonably similar across oils.
Notes: Updated

## Slide 33: Sqrt(AvPIE+0.5) ~ Oil Residual Plot by Oil
There variance appears reasonably similar across oils.
Notes: Updated

## Slide 34: Repeatability Limits
The following tables show examples of repeatability limits at various response levels. This shows the maximum difference of two repeated results before being considered statistically different at the 5% level of significance.
Low | High
0.00 | 0.79
5.00 | 9.74
15.00 | 27.64
Low | High
0.00 | 1.71
5.00 | 9.26
15.00 | 21.74
Ln(AvPIE+1)~Oil, Lab
Sqrt(AvPIE+0.5)~Oil, Lab
Realized values will end in a multiple of 0.25, but unrounded values are shown here for better comparison.
Notes: Updated

## Slide 35: Comparing raw standard deviations
The following tables show the raw standard deviations by oil. Clearly, the Sqrt transformation does a better job of stabilizing the variance across all oil levels.
Oil | Std. Dev.
220 | 0.3162
221 | 0.1931
222 | 0.1176
Oil | Std. Dev.
220 | 0.2425
221 | 0.3609
222 | 0.2694
Ln(AvPIE+1)~Oil
Sqrt(AvPIE+0.5)~Oil
Notes: Updated

## Slide 36
Analysis of Results
Using Ln(AvPIE+1) Transformation

## Slide 37: Ln(AvPIE +1) Plot by Oil/Engine
Plot of Ln(AvPIE + 1) by Oil and Engine, colored by lab
Variance appears to decrease as the response level increases, which may mean the transformation is not appropriate.
Notes: Updated

## Slide 38: Ln(AvPIE +1) ANOVA Full Model
Statistically significant differences:
Oil
Not significantly different:
Labs
Engines within Labs
Lab-Oil Interaction
Notes: Updated

## Slide 39: Ln(AvPIE +1) ANOVA Reduced Model
In this reduced model, the lab differences are still not statistically significant.
Notes: Updated

## Slide 40: Ln(AvPIE +1) Plot by Oil
Plot below is Ln(AvPIE + 1) by Oil and Lab, colored by lab
Notes: Updated

## Slide 41: Ln(AvPIE +1) Lab Differences
Model is Ln(AvPIE +1) ~ Oil, Lab
Plot below of Ln(AvPIE + 1) LSMeans by Lab, with 95% confidence intervals
Lab | Ln(AvPIE+1) LSMean | AvPIE LSMean
A | 1.9909 | 6.32
B | 1.8110 | 5.12
G | 1.9346 | 5.92
Lab1 | Lab2 | Ln(AvPIE+1) LSMean Difference | p-Value
A | B | 0.1798 | 0.29
G | B | 0.1235 | 0.58
A | G | 0.0563 | 0.76
LSMeans by Lab
LSMeans Differences Between Labs
Notes: Updated

## Slide 42: Ln(AvPIE +1) Oil Differences
Model is Ln(AvPIE +1) ~ Oil, Lab
Oil significantly differ
  All pairwise comparisons
    are statistically significant
  222 > 221 > 220
Plot shows Ln(AvPIE + 1) LSMeans by Lab,
with 95% confidence intervals
Oil | Ln(AvPIE+1) LSMean | AvPIE LSMean
220 | 0.3663 | 0.44
221 | 2.4734 | 10.86
222 | 2.8968 | 17.12
Oil1 | Oil2 | Ln(AvPIE+1) LSMean Difference | p-Value
222 | 220 | 2.5305 | <.0001
221 | 220 | 2.1071 | <.0001
222 | 221 | 0.4234 | 0.0002
LSMeans by Oil
LSMeans Differences Between Oils
Notes: Updated

## Slide 43: Ln(AvPIE +1) Oil Differences
Model is Ln(AvPIE +1) ~ Oil
Oil significantly differ
  All pairwise comparisons
    are statistically significant
  222 > 221 > 220
Plot shows Ln(AvPIE + 1) LSMeans by Lab,
with 95% confidence intervals
Oil | Ln(AvPIE+1) LSMean | AvPIE LSMean
220 | 0.3921 | 0.48
221 | 2.5085 | 11.29
222 | 2.9467 | 18.04
Oil1 | Oil2 | Ln(AvPIE+1) LSMean Difference | p-Value
222 | 220 | 2.5545 | <.0001
221 | 220 | 2.1164 | <.0001
222 | 221 | 0.4381 | 0.0001
LSMeans by Oil
LSMeans Differences Between Oils
Notes: Updated

## Slide 44: Ln(AvPIE +1) Precision
Model: Ln(AvPIE+1) ~ Oil, Lab
Model RMSE
= 0.2085
Model RMSE
Repeatability
= 0.2085 r = 0.5779
Repeatability
Reproducibility
= 0.2101 R = 0.5824
Reproducibility
Based upon the LSPI pooled standard deviation () and ASTM’s repeatability (r), there is no significant difference between an AvPIE of 5.00 and 9.50.
Note 1: An AvPIE result of 5.0 was arbitrarily selected as the pass/fail limit
Model: Ln(AvPIE+1) ~ Oil
Notes: Updated

## Slide 45: Ln(AvPIE +1) Precision
Model RMSE
= 0.2101
Model RMSE
Repeatability
= 0.2101 r = 0.5824
Repeatability
Reproducibility
= 0.2101 R = 0.5824
Reproducibility
Based upon the LSPI pooled standard deviation () and ASTM’s repeatability (r), there is no significant difference between an AvPIE of 5.00 and 9.50.
Note 1: An AvPIE result of 5.0 was arbitrarily selected as the pass/fail limit
Model: Ln(AvPIE+1) ~ Oil
Notes: Updated

## Slide 46: Reference Oil Targets
Ref. Oil | Target | St. Dev | RMSE
220 | 0.3663 | 0.2965 | 0.2085
221 | 2.4734 | 0.2097 | 0.2085
222 | 2.8968 | 0.1038 | 0.2085
  Average Number of Preignition Events (AvPIE)
  Unit of Measure: Ln(AvPIE +1)
Model: Ln(AvPIE+1) ~ Oil, Lab

## Slide 47: Reference Oil Targets
Ref. Oil | Target | St. Dev | RMSE
220 | 0.3921 | 0.3162 | 0.2101
221 | 2.5085 | 0.1931 | 0.2101
222 | 2.9467 | 0.1176 | 0.2101
  Average Number of Preignition Events (AvPIE)
  Unit of Measure: Ln(AvPIE +1)
Model: Ln(AvPIE+1) ~ Oil

## Slide 48
Analysis of Results
Using Sqrt(AvPIE+0.5) Transformation

## Slide 49: Sqrt(AvPIE+0.5) Plot by Oil/Engine
Plot of Sqrt(AvPIE+0.5) by Oil and Engine, colored by lab
Notes: Updated

## Slide 50: Sqrt(AvPIE+0.5) ANOVA Full Model
Statistically significant differences:
Oil
Not significantly different:
Labs
Engines within Labs
Lab-Oil Interaction
Notes: Updated

## Slide 51: Sqrt(AvPIE+0.5) ANOVA Reduced Model
In this reduced model, the lab differences are still not statistically significant.
Notes: Updated

## Slide 52: Sqrt(AvPIE+0.5) Plot by Oil, Lab
Plot below is Sqrt(AvPIE+0.5) by Oil and Lab, colored by lab
Notes: Updated

## Slide 53: Sqrt(AvPIE+0.5) Lab Differences
Model is Sqrt(AvPIE+0.5) ~ Oil, Lab
Plot below of Sqrt(AvPIE+0.5) LSMeans by Lab, with 95% confidence intervals
Lab | Ln(AvPIE+1) LSMean | AvPIE LSMean
A | 2.9968 | 8.48
B | 2.8062 | 7.37
G | 2.8376 | 7.55
Lab1 | Lab2 | Ln(AvPIE+1) LSMean Difference | p-Value
A | B | 0.1906 | 0.46
A | G | 0.1592 | 0.31
G | B | 0.0314 | 0.98
LSMeans by Lab
LSMeans Differences Between Labs
Notes: Updated

## Slide 54: Sqrt(AvPIE+0.5) Oil Differences
Model is Sqrt(AvPIE+0.5) ~ Oil, Lab
Oil significantly differ
  All pairwise comparisons
    are statistically significant
  222 > 221 > 220
Plot shows Sqrt(AvPIE+0.5) LSMeans by Lab,
with 95% confidence intervals
Oil | Ln(AvPIE+1) LSMean | AvPIE LSMean
220 | 0.9678 | 0.44
221 | 3.4145 | 11.16
222 | 4.2583 | 17.63
Oil1 | Oil2 | Ln(AvPIE+1) LSMean Difference | p-Value
222 | 220 | 3.2905 | <.0001
221 | 220 | 2.4467 | <.0001
222 | 221 | 0.8437 | <.0001
LSMeans by Oil
LSMeans Differences Between Oils
Notes: Updated

## Slide 55: Sqrt(AvPIE+0.5) Oil Differences
Model is Sqrt(AvPIE+0.5) ~ Oil
Oil significantly differ
  All pairwise comparisons
    are statistically significant
  222 > 221 > 220
Plot shows Sqrt(AvPIE+0.5) LSMeans by Lab,
with 95% confidence intervals
Oil | Ln(AvPIE+1) LSMean | AvPIE LSMean
220 | 0.9985 | 0.50
221 | 3.4476 | 11.39
222 | 4.3132 | 18.10
Oil1 | Oil2 | Ln(AvPIE+1) LSMean Difference | p-Value
222 | 220 | 3.3147 | <.0001
221 | 220 | 2.4491 | <.0001
222 | 221 | 0.8656 | <.0001
LSMeans by Oil
LSMeans Differences Between Oils
Notes: Updated

## Slide 56: Sqrt(AvPIE+0.5) Precision
Model: Sqrt(AvPIE+0.5) ~ Oil, Lab
Model RMSE
= 0.2813
Model RMSE
Repeatability
= 0.2813 r = 0.7797
Repeatability
Reproducibility
= 0.2856 R = 0.7916
Reproducibility
Based upon the LSPI pooled standard deviation () and ASTM’s repeatability (r), there is no significant difference between an AvPIE of 5.00 and 9.25.
Note 1: An AvPIE result of 5.0 was arbitrarily selected as the pass/fail limit
Model: Sqrt(AvPIE+0.5) ~ Oil
Notes: Updated

## Slide 57: Sqrt(AvPIE+0.5) Precision
Model RMSE
= 0.2856
Model RMSE
Repeatability
= 0.2856 r = 0.7916
Repeatability
Reproducibility
= 0.2856 R = 0.7916
Reproducibility
Based upon the LSPI pooled standard deviation () and ASTM’s repeatability (r), there is no significant difference between an AvPIE of 5.00 and 9.25.
Note 1: An AvPIE result of 5.0 was arbitrarily selected as the pass/fail limit
Model: Sqrt(AvPIE+0.5) ~ Oil
Notes: Updated

## Slide 58: Reference Oil Targets
Ref. Oil | Target | St. Dev | RMSE
220 | 0.9678 | 0.2453 | 0.2813
221 | 3.4145 | 0.3569 | 0.2813
222 | 4.2583 | 0.2397 | 0.2813
  Average Number of Preignition Events (AvPIE)
  Unit of Measure: Sqrt(AvPIE+0.5)
Model: Sqrt(AvPIE+0.5) ~ Oil, Lab

## Slide 59: Reference Oil Targets
Ref. Oil | Target | St. Dev | RMSE
220 | 0.9985 | 0.2425 | 0.2856
221 | 3.4476 | 0.3609 | 0.2856
222 | 4.3132 | 0.2694 | 0.2856
  Average Number of Preignition Events (AvPIE)
  Unit of Measure: Sqrt(AvPIE+0.5)
Model: Sqrt(AvPIE+0.5) ~ Oil

## Slide 60
Appendix 1: Evaluating the Engine Hours Effect

## Slide 61: Ln(AvPIE +1) Engine Hours Effect
The significance of the engine hours term is dependent on the model used.
Ln(AvPIE +1) ~ Oil, Lab, EngineHours
Ln(AvPIE +1) ~ Oil, EngineHours
Ln(AvPIE +1) ~ Oil, Lab, Engine[Lab], EngineHours
Notes: Updated

## Slide 62: Ln(AvPIE +1) Residuals by Engine Hours
Model is Ln(AvPIE +1) ~ Oil, Lab, Engine[Lab], EngineHours
There is no observable trend in the residuals in the first 500 hours, with potential concern arising above 600 hours, where all 4 residuals are negative.
Notes: Updated

## Slide 63: Sqrt(AvPIE + 0.5) Engine Hours Effect
The significance of the engine hours term is dependent on the model used.
Sqrt(AvPIE+0.5) ~ Oil, Lab, Engine[Lab], EngineHours
Sqrt(AvPIE+0.5) ~ Oil, EngineHours
Sqrt(AvPIE+0.5) ~ Oil, Lab, EngineHours
Notes: Updated

## Slide 64: Sqrt(AvPIE + 0.5) Residuals by Engine Hours
Model is Ln(AvPIE +1) ~ Oil, Lab, Engine[Lab], EngineHours
Though there is no clear trend, the two high residuals early in the engine life, along with the two low residuals late in the engine life, are potential areas of concern.
Notes: Updated

## Slide 65
Appendix 2: Additional Plots

## Slide 66: Ln(AvPIE +1) ~ Oil Residual Plot by Stand
There are two results that falls just outside the range of +/- 2, both on oil 220. The variability of 220 appears to be greater than the other oils, further supporting an alternative transformation.
Notes: Updated

## Slide 67: Sqrt(AvPIE + 0.5) ~ Oil Residual Plot by Stand
There is one result that falls just outside the range of +/- 2
Notes: Updated